Flow Pattern in the Estuary of Musi River                Using MIKE-21 Flow Model

Achmad Syarifudin1, Eka Puji Agustini1

1Bina Darma University, Palembang South Sumatra, Indonesia,

syarifachmad6080@yahoo.co.id, eka_puji@binadarma.acid

Abstract. Musi river which is the largest river with a length of more than 750 kilometers with an average width of 540 meters where the maximum width of 1,350 meters is located around the Kemaro island. Basically, sedimentation in the Musi river does include sedimentation due to the high level meeting between the Musi river currents and ocean currents in the Bangka Strait. Musi river silting conditions more severe because the sludge reaches about 40 cm per month. In fact, the volume of sludge could reach 2.5 million meter³. Along the Musi river shipping channel from the Boom Baru port to Bangka Strait there are 13 points silting.
Four points are already very vulnerable, because of the silting up to 4 meters. The location was quite prone to it the Island Umbrella northern and Muara cold compress, while the location of the experienced silting most severe among others on the verge outside, the mouth of the strait Jaran and the waters of the southern part of the Payung island sedimentation groove reaches 7 km, so the boat that crosses the groove Musi river should be guided against the tide that occurs.
This research was conducted with the approach of software models MIKE 21 Flow Model and the results obtained from this study is the pattern of movement of the flow between the other direction and speed of currents and hydrodynamic model the depth of the river starting from the verge outside to the Musi river which affected the tide downs.

1   Introduction

Musi river which is the largest river with a length of 750 kilometers and an average width of 540 meters (the width of the longest 1,350 meters) are located around the Kemaro island and (the shortest width of 250 meters) are located around the Musi Bridge II. Musi river has two islands, namely Kembaro (Kemaro) and Kerto islands. These three other major river is the Ogan river with an average width of 236 meters, Ogan river with an average width of 211 meters and the Keramasan river with an average width of 103 meters (Department of Public Works BM & NRM Palembang, 2012).
Musi river is not only used by people around the course. but also by large companies who live around the Musi river. They use the Musi river to deliver the products and bring in the raw material through the vessel. So many big ships and even very large pacing in this Musi river. Some companies located along the Musi river is PT. Pertamina, PT. Sriwijaya fertilizer (PUSRI), Wilmar Group and the Port of Boom Baru, and Port at 35 ilir. The role of the Musi river which is very vital in the life of so called pulse of Palembang city now starting at haunted various problems, one problem is silting continues the river to increase every year. Of course this is very detrimental to the Government of South Sumatra Province, especially at this time of South Sumatra province being intensively attract investors to invest in the business sector. Basically, sedimentation in the Musi river does include a high level of sedimentation caused by the current meeting between Musi river and ocean currents in the Bangka Strait.
Musi river silting conditions more severe because the sludge reaches about 40 cm per month. In fact, the volume of sludge could reach 2.5 million meter³. Along the Musi River shipping channel from the Boombaru Port to Bangka Strait there are 13 points silting. Four points are already very vulnerable, because of the silting up to 4 meters. The location was quite prone to it that in the northern part of the Payung island and the estuary, while locations that experienced the most severe silting among others on the verge outside, the mouth of the strait distance and the waters along the southern part of long the payung island, sedimentation that can reach 7 km. so that ships that cross the Musi river should be guided towards the waters tidal of the Musi river.

2   Methodology

This study will be carried out with the modeling and simulation of flow patterns and sediment transport in the waters of the Bangka Strait  in position 2.07º - 2.38º LS and 104.85º - 105.17º BT. The research location as in figure 1.

Fig. 1. Map of Research Location (Source: BPSDA, 2010)

3   Tools and Materials

The tools will be used in this research are as in Table 1 below

Table 1. List of the tools used in the study

| No | Name of Tools | Number of Uses |
| --- | --- | --- |
| 1 | Stationery 2 pieces | Writing to recording data |
| 2 | Computer (RAM 2 GB) 1 unit | Performing general modeling |
| 3 | Printer 1 unit | Displaying form of report |
| 4 | Software MIKE-21 Model, MS-Excel | Performing modeling and data processing |
| 5 | Dongle (licensed program) 1 pieces | Activating the software MIKE-21 FM |
| 6 | Laptop and Printer 1 pieces | Assisting to preparing reports |

The data used in the analysis as shown in Table 2.

Table 2. Types and Sources of Data Required

| No | Data properties | Data type | Sources | Units |
| --- | --- | --- | --- | --- |
| 1 | Tidal | Primary | Field | m |
| 2 | Bathymetry | Secondary | Bakosurtanal/Pelindo | m |
| 3 | The direction and speed of current | Primary | Field | (°) & m/s |
| 4 | River capasity | Primary | Field | m3/s |
| 5 | The direction and speed of wind | Secondary | BMG | (°) & m/s |
| 6 | Base of Sediment | Primary | Field | mm or ø |
| 7 | The concentration of suspended sediment | Primary | Field | mm/l |
| 8 | Discharge of sediment from the river | Primary | Field | gram/s |

4   MIKE-21 FM Simulation

MIKE-21 Hydrodynamic Module (HD Module) is a mathematical model to calculate the hydrodynamic behavior of the water against a wide variety of styles functions, for example certain wind conditions and water levels are specified in the open model of the boundary. HD module simulates the water level and the current differences in the various styles function in lakes, estuaries, and beaches.

5   Results and Discussion

Output Model Hydrodynamics
After all the boundary condition are met in the modeling, the results of global model output on the verge outside the Musi river as in figure 2, figure 3 and figure 4 as shown below.

Fig. 2. The hydrodynamic model of the river water velocity direction

Fig. 3. Model hydrodynamic surface elevation watersheds

Fig. 4. The total depth of the hydrodynamic model of river flow

6   Conclusions and Recommendations

From the analysis of this study can be summarized as follows:

- Direction speed greatest occurred on the Musi river mouth ranged between 300-350 degrees.

- Outer surface elevation of the threshold Musi river ranges between 0.20 m - 0.40 m, it will affect the free area for ships to perform well and safe movement.

- The total depth of water occurs at 15-30 m and therefore contributes to the flow of the ship movement into the Musi river as a whole.

As a recommendation of this study is necessary to study more detail about the correlation of sediment movement and move of the ship to the amount of sediment in the Musi river.

Acknowledgments

I would like to say thank to Prof. Ir. Bochari H. Rachman, M.Sc, Rector of Bina Darma University, Prof. Dr. H. Zainuddin Ismail, MM, Vice Rector I and Dr. Sunda Ariana, MM, M Ed, Vice Rector II of Bina Darma University are pleased to give permission and assistance to the author, especially in the preparation of the data so that the paper can be completed.

References

- Hartayo Suprianto, Sumarjo Gatot Irianto, Robiyanto H. Susanto, and FX BartSchult. Suryadi 2006, Potential and constrains of water management measures for tidal lowlands in South Sumatra. Case study in a pilot area Telang I. In proceedings of the 9th Inter-Regional Confrence on the water environment. Enviro water, Concept for Water management and multifunctional land uses in lowlands, Delft, the Netherlands.

- Harinaldi 2005, Principles of Statistics for Engineering and Science, Erland Jakarta, Indonesia.

- Indarto 2010, Hydrology, Basic Theory and Application Example Model Hydrology, PT. Earth Literacy, Jakarta, Indonesia Joint Working Group, Ministry of Public Works and Rijkwaterstaat., 2005. Technical Guidelines On Tidal Lowland Development. Volume II: Water Management.

- Munir, S 2010, Role of sediment transport in operation and maintenance of supply and demand based irrigation canals, PhD Thesis UNESCO-IHE, Delft, The Netherlands.

- Paudel, 2010, Role of sediment in the design and management of irrigation canals, Sunsari Morang Irrigation Scheme, Nepal, PhD Thesis, UNESCO-IHE, Delft, The Netherlands.

- Schultz, B and Vries, WS, 1993. The 15th Congress on Irrigation and Drainage: Water Management in the Next Century: Q.45 R.17: Some Aspects of Maintenance Typical Drainage Systems in Flat Areas. The Hague.

- Schultz, E. 1993. Land and Water Development: Finding a balance between implementation, management and sustainability. IHE Delft. Netherlands.

- Schultz, B, Zimmer, D, and Vlotman, WF, 2007. Drainage under Increasing and Changing Requirements. The Journal of the International Commission on Irrigation and Drainage. John Wiley and Sons Ltd.

- Supriyanto, H., 2004. Where do We Stand on Swamplands Development. Regional Seminar on Teaching Tidal Lowlands.

- Supriyanto, H, Irianto, SG, Susanto, RH, Suryadi, FX, Schultz, B., 2006. Potentials and Constraints of Water Management Measures for Tidal Lowlands in South Sumatra. Case Study in a Pilot Area in Telang I. In Proceedings of the 9th Inter-Regional Conference on Environment-Water. Delft.The Netherlands.

- Suryadi, FX, October 1996. Soil and Water Management Strategies for Tidal Lowlands in Indonesia. Netherlands, A.A. Balkema, Rotterdam. The Netherlands.

- Suryadi, FX, 2004. Development of Tidal Wetlands in South Sumatra Swamp Experience Regional Development and O & M Telang I.Land and Water Management Tidal Lowlands.

- Suryadi, F.X, 2007. Lecture Notes. Unsteady flow. Unesco IHE. The Netherlands.

- Djajamurni 2008, policy development and management of swamp (now and in the future), Papers in the Workshop on the Strengthening of Tidal Lowland Development (STLD), Jakarta. Indonesia

# Text boxes

Research location